## Slide 1
RCON MotionAI
01
RCON
MotionAI
Turning skilled construction movement into machine-readable motion intelligence
Capture → Convert → Visualize → Analyze → Classify
Client prototype update · September 2026
👷‍♂️ → 🧠 → 🤖
Human motion capture + AI
for the built environment
Rokoko suit + Smartgloves
Real construction-task recordings
First activity-recognition model
Notes: Open with one sentence: MotionAI turns construction movement into structured motion data that AI can understand. Mention this now uses real Rokoko recordings.

## Slide 2
RCON MotionAI
02
PROBLEM
Construction skill is physical — most AI data is not
MotionAI targets the missing data layer between human trade skill and machine intelligence.
•
Skilled work happens through motion: posture, reach, repetition, tool use, grip, timing.
•
Most construction AI works from text, images, plans, or video — not precise body motion.
•
Training, safety, digital twins, and robotics all need structured human-motion data.
Human Skill
👷
→
Missing
Motion Layer
→
AI / Robots
🤖
↓
MotionAI creates the missing layer by converting human construction movement into standardized data.
Notes: Keep this slide construction-focused. The problem is not animation; the problem is that physical skill is not captured in AI-ready form.

## Slide 3
RCON MotionAI
03
STATUS
What we built: a working motion intelligence pipeline
Current milestone: real capture data goes through conversion, visualization, feature extraction and classification.
Capture
Rokoko + gloves
→
Convert
FBX → JSON
→
Visualize
3D skeleton
→
Analyze
415 features
→
Classify
AI prediction
25
real recordings
5
activity classes
75
bones/frame
415
features/recording
100%
pilot CV accuracy
single actor
This is no longer synthetic-only: MotionAI now processes real movement captured from the Rokoko suit and Smartgloves.
Notes: This is the headline project-status slide. Spend a little time here because it tells them the prototype is real.

## Slide 4
RCON MotionAI
04
ARCHITECTURE
The system is built around a reusable MotionSession format
Rokoko plugs into the input side; viewer, dataset tools and AI work from a standard representation.
Rokoko
FBX export
→
Blender
extraction
→
MotionAI
JSON
→
MotionSession
standard format
From the same MotionSession:
3D Viewer
AI Features
+ Classifier
Future Avatar
/ Robotics
The adapter architecture prevents the project from becoming a one-off Rokoko demo.
Notes: Emphasize: if we change mocap devices later, we change the adapter, not the whole system.

## Slide 5
RCON MotionAI
05
DATASET
Initial construction-motion pilot dataset
Five activities, five recordings per activity, captured with Rokoko body suit + Smartgloves.
Activity
Clips
Motion signal
Box Carry
5
movement through space
Box Lift
5
bend, grasp, lift
Hammer Strike
5
repeated tool motion
Material Place
5
reach, place, release
Overhead Work
5
arms above shoulder level
👷‍♂️ + 🧤
75 bones per frame
including hand and finger motion from Smartgloves
Next dataset need: multiple participants performing the same task set.
Notes: Call it an initial pilot dataset. The next research step is multiple actors.

## Slide 6
RCON MotionAI
06
DEMO 1
Visualize real captured movement
The MotionAI viewer reconstructs captured body motion from standardized JSON.
Run:
python -m src.visualization.skeleton_viewer data\processed\box_lift_001.json
•
Real recording captured in Rokoko Studio and exported as FBX.
•
Converter extracts 3D body and hand-bone motion into MotionAI JSON.
•
Viewer plays it back with 3D skeleton, metadata and playback controls.
3D Skeleton Playback
👷‍♂️ → 📦 → table
Play / Pause / Restart
Key line for the demo: “This is a real Rokoko capture running through our own MotionAI pipeline.”
Notes: Open the viewer live. Point out that it is real capture data. Keep this simple and visual.

## Slide 7
RCON MotionAI
07
MACHINE LEARNING
MotionAI turns movement into 415 AI features
The first model uses engineered features to classify construction activities from motion patterns.
MotionAI JSON
75 bones/frame
→
Preprocess
root-center + normalize
→
Feature Vector
415 values
→
Random Forest
classifier
Feature groups
Joint position
mean, std, min/max, range
Joint velocity
mean absolute velocity, max velocity
Whole-body motion
pelvis displacement and movement range
Duration
how long the task took
Why a Random Forest first?
Fast, explainable, strong with small datasets, and outputs class confidence scores.
Notes: Say this is the baseline model. More advanced sequence models can come later after the dataset is larger.

## Slide 8
RCON MotionAI
08
DEMO 2
Classify a motion recording
MotionAI predicts the activity directly from skeletal motion features.
Run:
python -m Scripts.test_activity_classifier data\processed\hammer_strike_005.json
Prediction
Hammer Strike
96.40% confidence
Class probabilities
Hammer Strike
96.4%
Material Place
1.2%
Overhead Work
1.2%
Box Lift
0.8%
Box Carry
0.4%
The model is recognizing task-specific movement patterns from motion capture data, not video imagery.
Notes: After showing the viewer, run this classifier command. Then transition to the cross-validation result as the stronger evaluation.

## Slide 9
RCON MotionAI
09
EVALUATION
Pilot evaluation: 100% out-of-fold accuracy
Five-fold stratified cross-validation across 25 single-actor recordings.
5
folds
25/25
correct predictions
83.96%
avg confidence
0
misclassifications
5
activity classes
Aggregate confusion matrix
Carry
Carry
5
0
0
0
0
Lift
Lift
0
5
0
0
0
Hammer
Hammer
0
0
5
0
0
Place
Place
0
0
0
5
0
Over
Over
0
0
0
0
5
How to say it
“In an initial single-actor pilot dataset, MotionAI achieved 100% out-of-fold activity-classification accuracy across five construction activities.”
Important scope: single actor, controlled tasks. Next validation is multi-person and more variable conditions.
Notes: Say the careful result exactly. This protects credibility while still being impressive.

## Slide 10
RCON MotionAI
10
CONSTRUCTION VALUE
Where this can create value
The same motion layer can support training, safety, workflow analysis, digital twins and robotics research.
Skill capture
Record how experienced workers perform physical tasks.
Training
Compare apprentice motion against expert motion.
Ergonomics
Detect risky bending, reaching, repetition and posture.
Digital twins
Replay real worker activity inside virtual environments.
Task recognition
Identify construction activities from body motion.
Future robotics
Use human demonstrations as research data for machines.
Client decision point: which use case should become the first real pilot?
Notes: Invite feedback. Ask which application would be most valuable to the client.

## Slide 11
RCON MotionAI
11
NEXT STEPS
Recommended next phase: validate and productize
The foundation works. The next goal is proving generalization and turning results into a client-ready demo flow.
1
Multi-worker capture
3–5 people perform the same task set
2
Generalization test
Train on some workers, test on a new person
3
Prediction UI
Show activity + confidence beside the motion viewer
4
Use-case focus
Choose training, safety, productivity, or robotics path
What we need from the client
1. Which tasks matter most?
2. What outcome is most valuable?
3. Who can help perform/validate motions?
4. What would make the R-CON demo useful?
Goal: prototype → pilot
Notes: Finish with a clear ask. You want the client to help choose task priorities and validation criteria.

## Slide 12
RCON MotionAI
12
MotionAI v0.2
Real Rokoko capture → standardized motion data → 3D visualization → AI activity recognition
Initial single-actor pilot: 25 recordings, 5 construction activities, 100% out-of-fold classification accuracy.
Questions + feedback
What should MotionAI prove next?
Capture → Convert → Visualize → Analyze → Classify
Notes: Close by inviting feedback and direction for the next validation phase.